## Slide 1
Robotics Club - Workshop 1

## Slide 2
Robotics Club - Workshop 1

## Slide 3
Table of Contents
1. What is a Robot?
2. Introduction to Arduino
3. Digital vs Analog
4. Components of Arduino
5. Sensors and Actuators
6. Setting Up First Project

## Slide 4
1. What is a Robot?
Mobile Robot
Stationary Robot
Humanoid Robot

## Slide 5
1. What is a Robot?
Environmental
Sensor
Controller
Actuator

## Slide 6
2. Introduction to Arduino
  What is Arduino?
  Arduino is an open-source platform used for building electronics projects. It consists of both a programmable circuit board (microcontroller) and software (Arduino IDE) to program it.

## Slide 7
  Why Learn Arduino?
  Arduino makes electronics easy to learn because it allows users to control hardware with simple code. It’s widely used in DIY projects, education, and even in professional prototyping.
2. Introduction to Arduino

## Slide 8
3. Digital vs Analog
Digital Signal
Analog Signal

## Slide 9
4. Components of Arduino
1. MICROCONTROLLER
2. USB PORT
3. USB TO SERIAL CHIP
4. DIGITAL PINS
5. ANALOG PINS
6. VIN
7. 5V/3.3V
8. GND

## Slide 10
Touch Sensor
3
5. Sensors and Actuators
IR (InfraRed) Sensor
1
LDR (Light Dependent Resistor) Sensor
2
Ultrasonic Sensor
4
Sound Sensor
5
Joystick Module
6

## Slide 11
  Step 1:
  Understanding the Components
  Step 2:
  Circuit Setup
  Step 3:
  Code
  Step 4:
  Upload the Code
6. Setting Up First Project

## Slide 12
6. Setting Up First Project
DC Motor
2
Arduino board
1
L298N Motor Driver Module
3
Jumper wires
4
Mobile Robot Chassis Kit
6
USB cable
5
Battery
7
  Step 1:
  Understanding the Components

## Slide 13
6. Setting Up First Project
1. Why Motor Driver Module?
  Step 1:
  Understanding the Components
A Motor Driver is an electronic component that controls the operation of DC motors, allowing you to control the speed and direction of the motors using a low-power microcontroller, like an Arduino.
The L298N is a dual H-Bridge motor driver. An H-Bridge is a circuit that allows you to control the direction of a DC motor.

## Slide 14
6. Setting Up First Project
  Step 1:
  Understanding the Components
H-Bridge DC Motor Control
For controlling the rotation direction, we just need to inverse the direction of the current flow through the motor, and the most common method of doing that is by using an H-Bridge. An H-Bridge circuit contains four switching elements, transistors or MOSFETs, with the motor at the center forming an H-like configuration. By activating two particular switches at the same time we can change the direction of the current flow, thus change the rotation direction of the motor.

## Slide 15
6. Setting Up First Project
2. Pins and Connections of L298N
  Step 1:
  Understanding the Components
[1] Input Control Pins:
[A] IN1 and IN2 (for Motor 1)
[B] IN3 and IN4 (for Motor 2)
Role: Control the direction of Motor 1 / Motor 2 (forward/reverse).
Depending on the HIGH/LOW combination of IN1, IN2, IN3 and IN4 , Motor 1/ Motor 2 can move forward or backward.

## Slide 16
6. Setting Up First Project
2. Pins and Connections of L298N
  Step 1:
  Understanding the Components
[2] Enable Pins (Speed Control):
These pins control the speed of the motors using PWM signals from the Arduino.
[A] ENA (Enable A): This pin enables or disables Motor 1. By connecting it to a PWM pin on the Arduino and using analogWrite(), you can control the speed of Motor 1.
[B] ENB (Enable B): This pin enables or disables Motor 2. It can also be connected to a PWM pin to control Motor 2's speed.

## Slide 17
6. Setting Up First Project
2. Pins and Connections of L298N
  Step 1:
  Understanding the Components
[3] Power Pins:
[A] 12V
[B] GND (Ground)
[C] 5V
[4] Motor Control Pins:
[A] OUT1 and OUT2
[B] OUT3 and OUT4

## Slide 18
6. Setting Up First Project
3. How the L298N Works
  Step 1:
  Understanding the Components
Motor Direction
Each motor has two input pins (e.g., IN1/IN2 for Motor 1). By setting one pin HIGH and the other LOW, you control the direction in which the motor spins.
For example:
  IN1 HIGH, IN2 LOW → Motor moves forward.
  IN1 LOW, IN2 HIGH → Motor moves backward.
Motor Speed
The ENA and ENB pins are used to control the speed of the motors using PWM. By applying a PWM signal (with a value between 0 and 255) to these pins, you can vary the motor speed. A value of 0 turns the motor off, and 255 runs it at full speed.

## Slide 19
  Step 2:
  Circuit Setup
6. Setting Up First Project
Right Motor (Motor 1)
IN1 (Motor 1) ← Arduino Pin 3
IN2 (Motor 1) ← Arduino Pin 4
ENA (Motor 1) ← Arduino Pin 2 (PWM Pin)
OUT1 and OUT2 ← Motor 1 Pin 1-2
Left Motor (Motor 2)
IN3 (Motor 2) ← Arduino Pin 5
IN4 (Motor 2) ← Arduino Pin 6
ENB (Motor 2) ← Arduino Pin 7 (PWM Pin)
OUT3 and OUT4 ← Motor 2 Pin 1-2
Battery
The positive terminal ← 12V pin on the L298N.
The negative terminal ← GND pin on the L298N and Arduino.
5V terminal ← Arduino Pin 5V/VIN

## Slide 20
6. Setting Up First Project
  Step 2:
  Circuit Setup

## Slide 21
  Step 3:
  Code
6. Setting Up First Project

## Slide 22
  Step 3:
  Code
6. Setting Up First Project

## Slide 23
  Step 3:
  Code
6. Setting Up First Project

## Slide 24
  Step 3:
  Code
6. Setting Up First Project

## Slide 25
  Step 4:
  Upload the Code
6. Setting Up First Project
Open the Arduino IDE.
Connect the Arduino board.
Select the correct board and port:
Go to Tools > Board and select the correct Arduino model.
Go to Tools > Port and select the COM port.
Copy and paste the code into the Arduino IDE.
Click the Upload button.

## Slide 26
Drive Link

## Slide 27
Thank You.
Robotics Club - Workshop 1
Youssef Adel
Instagram
LinkedIn
Facebook
WhatsApp